Study of an inverse problem that models the detection of corrosion in metalic plate whose lower part is embedded

SAIDMohamed Said*

Laboratoire LMA University of Kasdi Merbah Faculty of Sciences and technology Ouargla, 30000 Ouargla  Algeria

Abstract

In this work, we will study an inverse problem to determine corrosion in an inaccessible location of a metalic plate. Our study area is inside the plate metalic plate whose lower part is embedded therefore inacssecible. We will perform measurements on the upper part of the plate, which is not in contact with the ground. For this, we will send an electric field on this part and take measurements. This problem is modeled by a Laplace problem with mixed presence of an unknown term in the boundary conditions this term is an unknown function which can take several forms. It is this function that we will detect the presence or absence of corrosion inside the tube and we will then follow our steps to the top edge of the field information on the evolution of this corrosion. We will first formulate our problem which is an inverse problem and we will make a theoretical study and we will that this problem has a unique solution also this solution is stable. After, we will solve this problem by constructing an iterative algorithm which gives problems that will cross a series of impedance functions which determines the rate of corrosion. Finally we study the convergence and we will then make a numerical application

© 2012 Published by Elsevier B.V.

Keywords: corrosion;  inverse problem; electric potential;  harmonic function; imppedence

Introduction

Let  , and is the border of . The boundary  is decomposed into four disjoint open  where:

; ;; 
we assume that  is the part embedded of , therefore inacssecible, then the boundary value on  is unknown. The electric potential u satisfies the foll owingdifferential equation

(1)

where the Dirichlet and Neumann value on  of the electric potential u are known and are  given

;                                       (2)
Where are two functions given in . Since  are known, we can easily solve the problem (1)-(2). The inaccessible part of the border is  that is supposed to be corroded, the appearance of any corrosion on  is modeled by a function 
It is therefore to find  such that

(3)

Our problem is :Find the fuctions  and  solution of the following problem:

(4)

Where  ,   then                                                                                    (5)

To solve the prolem (4), we will construct an algorithm that gives a good approximation of the function . This algorithme gives a sequence  of approximate values of the function.We will show that the sequence  converges to the function . Finally we make a numerical application by giving a concrete example.

2-Position of the Problem

In general the problems such as: Find a function u such that:

(6)

Where  is a bounded open in ,  and f is given in , being the border of , with the condition  , admit a unique solution at least in .

Indeed: We can for example apply the Lax Milgram theorem and we deduce that: the problem (6)  .   admit a unique solution in  .

But if the open  is convex, we show in[] that the problem (6) has a solution in at least in space . While the uniqueness is the variational uniqueness, shown  by using the Lax Milgram theorem.

The resolution of our prpoblem will made in several sreps.

First step  We solve the problem (1)-(2), and from the boundary values of this problem, ​​we want

to determine the boundaty values functions in (4), and therefore we determine the impedance function ( given by  the formula (5)

Second step: Construction of an iterative algorithm of resolution of the problem (4)

References

[1]P. Grisvard, Alternative of Fredholm relating to the problem of Dirichlet in a  polygon, Boll. Un. Mat. Ital. 5(4) (1972), 132-164

[2]P. Grisvard, Singularities in boundary values problem, Dunod Paris (1992)

[3]  BRESIS. H . Analyse Fonctionnelle  Masson  Paris 1983

[4]  J. Cheng M Chouli  X Yang  An iterative BEM method for the inverse problem of detecting corrosion in a pipe

numerical Mathematics  A journal of Chineese universities, Vol 14 N°3 Ang 2005

[5]  A Tveito , R Winter Introduction to partial differential equations a computitionnal approach springer 2008-

[6]  M Chouli introduction aux problèmes inverses elliptiques et paraboliques Springer Vering Berlin Heidlberg 2009

[7]  M Chouli Stability estimates for an inverse elliptic problem Journal of inverse problems 3 posed Prob,(10), 2002

N°6, 601-610

# Footnotes

* Corresponding author. Tel.: +213 662 67 4221; fax: +321 29712627.

E-mail address: smedsaid@yahoo.com.